## Slide 1: CubeSat mission: detection of space debris on LEO
Fantine Blanquez-Nadal
June 8th – September 8th

## Slide 2: Summary
Introduction
Tools used
Modeling work
Study of the orbit
Sizing of the thermal control system

## Slide 3: I. Introduction
Background of the project
The issue:
Space debris
How much ?
Mspace debris = 3000 t
Where ?
GEO (Geostationary Orbit), GTO (Geostationary Transfer Orbit), LEO (Low Earth Orbit)

## Slide 4: II. Tools used
FreeCAD
Ansys STK

## Slide 5: III. Modeling work
3D view of an experiment

## Slide 6: III. Modeling work
1st version: too much detailed  too heavy for STK
Not machinable
1st version of the external structure of the cubesat

## Slide 7: III. Modeling work
2nd draft: less detailed –> STK
2nd version of the external structure of the cubesat

## Slide 8: III. Modeling work
Visualization of the satellite on its orbit, STK

## Slide 9: IV. Study of the orbit
Criteria:
Sun-synchronous, 700 km < altitude < 900 km
Goal:
To have a trajectory where the satellite receives as much light as possible
Orientation of the satellite toward the sun

## Slide 10: IV. Study of the orbit
Formula:
p: the semi latus rectum: , e: eccentricity=0 and 
= : factor of Earth non-sphericity
: the variation of in 1 orbit;
i: the inclination
Inclination for a sun-synchronous orbit at 800 km
- : rotation of the Earth on itself
and


## Slide 11: IV. Study of the orbit
STK
Create a new scenario: sun-synchronous orbit + altitude of 800 km 
Chart: i=f(h)
| 700 | 720 | 740 | 760 | 780 | 800 | 820 | 840 | 860 | 880 | 900 | 920 | 940 | 960 | 980 | 1000 | 1020 | 1040 | 1060 | 1080 | 1100 | 1120 | 1140 | 1160 | 1180 | 1200 | 1250 | 1260 | 1280 | 1300 | 1305 | 1310 | 1320 | 1350 | 1370 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
 | 98.1928 | 98.2746 | 98.3571 | 98.4401 | 98.5237 | 98.608 | 98.6928 | 98.7783 | 98.8644 | 98.951 | 99.0384 | 99.1263 | 99.2148 | 99.304 | 99.3939 | 99.4843 | 99.5754 | 99.6671 | 99.7595 | 99.8526 | 99.9462 | 100.041 | 100.136 | 100.231 | 100.328 | 100.425 | 100.67 | 100.72 | 100.819 | 100.92 | 100.945 | 100.97 | 101.021 | 101.174 | 101.277 | 101.432 | 101.695 | 101.962 | 102.234 | 102.51 | 102.791 | 103.077 | 103.368 | 103.663 | 103.964 | 104.269 | 104.58 | 104.895
Inclination for a sun-synchronous orbit at 800 km

## Slide 12: IV. Study of the orbit
Local Time of Descending Node
LTDN = 12 a.m.  insufficient illumination
Figure explaining the descending node
Sun-synchronous orbit, 800 km, LTDN = 12 a.m.

## Slide 13: IV. Study of the orbit
Orbit: in the plane separating day and light (sunset)  LTDN = 6 p.m.
Local Time of Descending Node
Local Time of Descending Node | Time of total darkness (s)
12 a.m | 10901950,948
6 p.m | 741687,026
Sun-synchronous orbit, 800 km, LTDN = 6 p.m.

## Slide 14: IV. Study of the orbit
Local Time of Descending Node
Chart: t_shadow=f(LTDN), altitude = 800 km
| 0.125 | 0.14583333333333334 | 0.16666666666666666 | 0.1875 | 0.20833333333333334 | 0.22916666666666666 | 0.25 | 0.27083333333333331 | 0.29166666666666669 | 0.3125 | 0.33333333333333331 | 0.35416666666666669 | 0.375 | 0.39583333333333331 | 0.41666666666666669 | 0.4375 | 0.45833333333333298 | 0.47916666666666702 | 0.5 | 0.52083333333333304 | 0.54166666666666696 | 0.5625 | 0.58333333333333304 | 0.60416666666666596 | 0.625 | 0.64583333333333304 | 0.66666666666666596 | 0.6875 | 0.70833333333333304 | 0.72916666666666596 | 0.75 | 0.77083333333333304 | 0.79166666666666596 | 0.8125 | 0.83333333333333304 | 0.85416666666666596 | 0.875
ombre | 28.1539 | 24.4087 | 16.9585 | 7.5505 | 4.699 | 3.0679 | 2.4799 | 2.9533 | 4.4917 | 7.3305 | 17.2445 | 24.5233 | 28.2038 | 30.5796 | 32.1941 | 33.2937 | 34.0091 | 34.4131 | 34.5429 | 34.4097 | 34.0019 | 33.2818 | 32.1763 | 30.5541 | 28.1706 | 24.5021 | 17.8263 | 6.9778 | 4.3399 | 2.8235 | 2.3502 | 2.9308 | 4.5309 | 7.2096 | 17.4537 | 24.3903 | 28.1172
Best LTDN = 6 p.m.

## Slide 15: IV. Study of the orbit
Parametric study
Chart: t_shadow=f(h)
| 700 | 725 | 750 | 775 | 800 | 825 | 850 | 875 | 900
12:00 | 38.3383 | 35.2027 | 34.9776 | 34.7598 | 34.5429 | 34.3329 | 34.1252 | 33.9262 | 33.7233
13:00 | 37.7843 | 34.6881 | 34.4541 | 34.2274 | 34.0019 | 33.7832 | 33.567 | 33.3596 | 33.1484
14:00 | 35.9372 | 32.9554 | 32.6901 | 32.4324 | 32.1763 | 31.9273 | 31.6813 | 31.4442 | 31.2038
15:00 | 31.9242 | 29.1794 | 28.8373 | 28.503 | 28.1706 | 27.8455 | 27.5239 | 27.2107 | 26.8954
16:00 | 22.1726 | 19.8693 | 19.2028 | 18.5253 | 17.8263 | 17.1047 | 16.3469 | 15.5363 | 14.6156
17:00 | 5.1992 | 4.9702 | 4.7511 | 4.5412 | 4.3399 | 4.1468 | 3.9614 | 3.7833 | 3.6122
18:00 | 3.0868 | 2.891 | 2.7032 | 2.5231 | 2.3502 | 2.1842 | 2.025 | 1.8719 | 1.7249
For all altitudes varying between 700 km and 900 km, LTDN = 6 p.m. is the best.
Chart: t_shadow=f(LTDN)
| 0.66666666666666663 | 0.67708333333333337 | 0.6875 | 0.69791666666666696 | 0.70833333333333404 | 0.71875 | 0.72916666666666696 | 0.73958333333333404 | 0.750000000000001 | 0.76041666666666696 | 0.77083333333333404 | 0.781250000000001 | 0.79166666666666796 | 0.80208333333333504 | 0.812500000000001 | 0.82291666666666796 | 0.83333333333333504
h=700km | 22.1726 | 15.7305 | 9.339 | 6.4475 | 5.1992 | 4.2537 | 3.5877 | 3.1981 | 3.0868 | 3.2545 | 3.697 | 4.4095 | 2.2235 | 6.6665 | 8.5186 | 14.5786 | 21.6325
h=900km | 14.6156 | 8.2686 | 6.0669 | 4.7004 | 3.6122 | 2.772 | 2.1747 | 1.824 | 1.7249 | 1.8782 | 2.2799 | 2.9226 | 3.8006 | 4.9173 | 6.3007 | 8.0449 | 13.8093
h=800km | 17.8263 | 10.9369 | 6.9778 | 5.4986 | 4.3399 | 3.4522 | 2.8235 | 2.4549 | 2.3502 | 2.5102 | 2.9308 | 3.6055 | 4.5309 | 5.7172 | 7.2096 | 10.4983 | 17.4537

## Slide 16: IV. Study of the orbit
The higher the altitude, the smaller the time spent in the shadow.
~ 1300 km = no more time spent in darkness, but it’s too high.
Between 700 km and 900 km, only 2.75 % and 1.75% of the year is spent in darkness.
An altitude of 800 km is great.
Parametric study
Chart: t=f(h), LTDN=18:00:00.000 HMS
| 700 | 720 | 740 | 760 | 780 | 800 | 820 | 840 | 860 | 880 | 900 | 920 | 940 | 960 | 980 | 1000 | 1020 | 1040 | 1060 | 1080 | 1100 | 1120 | 1140 | 1160 | 1180 | 1200 | 1250 | 1260 | 1280 | 1300 | 1305 | 1310 | 1320 | 1350 | 1370 | 1400 | 1450 | 1500 | 1550 | 1600 | 1650 | 1700 | 1750 | 1800 | 1850 | 1900 | 1950 | 2000
ombre | 3.0868 | 2.9295 | 2.7773 | 2.6302 | 2.4879 | 2.3502 | 2.217 | 2.0879 | 1.963 | 1.8421 | 1.7249 | 1.6113 | 1.5013 | 1.3947 | 1.2913 | 1.1911 | 1.094 | 0.99993 | 0.90869 | 0.82023 | 0.73451 | 0.65138 | 0.5708 | 0.49276 | 0.4171 | 0.3438 | 0.17042 | 0.13735 | 0.072841 | 0.010368 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
pénombre | 0.34904 | 0.34951 | 0.3444 | 0.34448 | 0.33906 | 0.33686 | 0.33725 | 0.3317 | 0.33013 | 0.32768 | 0.32542 | 0.32319 | 0.32229 | 0.32044 | 0.31726 | 0.31572 | 0.31386 | 0.31247 | 0.31014 | 0.31139 | 0.30645 | 0.30539 | 0.3046 | 0.30167 | 0.30023 | 0.29866 | 0.29575 | 0.29443 | 0.29362 | 0.29384 | 0.28733 | 0.27126 | 0.23954 | 0.15124 | 0.094406 | 0.01305 | 0.01034 | 0.0097595 | 0.011712 | 0.012447 | 0.011924 | 0.012051 | 0.012472 | 0.011414 | 0.010042 | 0.011626 | 0.010771 | 0.008738

## Slide 17: V. Sizing of the thermal control system
Thermal environment of the satellite
Orbital parameters:
Sun-synchronous orbit
Altitude of 800 km  inclination of 98,608°
LTDN = 6 p.m.
Harsh environment but:
Fluxes to take into account
Pointing of the satellite

## Slide 18: V. Sizing of the thermal control system
The most common thermal control systems
Passive or active systems: surface finishes, MLI, heat pipes, louvers, radiators…
Surface finishes
MLI
Patch heater

## Slide 19: V. Sizing of the thermal control system
Methods described in 11.5 Thermal, section Radiator requirements, p. 453-456 (Space Mission Analysis and Design, J.R Wertz) + Spacecraft Systems Engineering, p.363
We determine equilibrium temperatures, in the hot and the cold case and for different surface finishes:
(1)
, , ,
is the solar radiation intensity
is the intensity of the incident albedo radiation.
is the intensity of the Earth IR radiation.
is the internal dissipated heat.
α, ε and σ respectively are the absorptance, the emissivity and the constant of Boltzmann.
1st method

## Slide 20: V. Sizing of the thermal control system
: radius of the Earth’s surface
: orbit radius
1st method
 | α | ε
Black paint | 0.9 | 0.9
White paint | 0.15 | 0.9
Electroplated gold | 0.25 | 0.04
MLI | 0.45 | 0.71
Earth albedo. ;
;
F: visibility factor  F=0.1
values of ε and α for different surface finishes

## Slide 21: V. Sizing of the thermal control system
Black paint | 9.2°C | -18°C
White paint | - 28°C | -69°C
Electroplated gold | 252°C | 153°C
MLI | 12°C | -44°C
Black paint | 9.2°C | -18°C
White paint | - 28°C | -69°C
Electroplated gold | 252°C | 153°C
MLI | 12°C | -44°C
1st method
Temperatures for different surface finishes in the cold case and in the hot case
The best surface finish: black paint.
Needs a heating system (-18°C <<< 0°C)

## Slide 22: V. Sizing of the thermal control system
Area of radiators:
: maximum temperature of internal components.
and were calculated previously. In the hot case, and
(black paint)

1st method
Very uncertain method

## Slide 23: V. Sizing of the thermal control system

We can’t really draw conclusions from this result. The model we used is too much simplified.
1st method
Very uncertain method

## Slide 24: V. Sizing of the thermal control system
Solving the heat transfer budget equation using explicit Euler:
2nd method
: capacitance,
: solar flux,
: albedo flux,
: IR Earth flux,
: internal heat dissipation flux
: external heating source flux
: conductive flux established between nodes i and k;
: radiative flux established between nodes i and j;
where is the view factor of surface j as seen from surface I and is the effective emittance.

## Slide 25: V. Sizing of the thermal control system
and can’t be neglected because the orbit is low, near the surface of the Earth.
In a CubeSat, the density of internal components is big: we will neglect radiative coupling  .
: not considered (1 node)
Encoding on python
Need values for , ,  I wasn’t able to go further
2nd method
Simple model: 1 node

## Slide 26: Conclusion