CubeSat mission for the detection of small-size space debris at Low Earth Orbit
INTERNSHIP FROM 06/01 TO 08/31
UNIVERSITY OF TORINO, PHYSICS DEPARTEMENT
DUPRAZ CELIA

---
Table of contents:
Subsystems
8U configuration
12U configuration
Link budget
Power budget
Cost budget
Mass budget
Final configuration / Summary

---
Propulsion system
Thrusters, feed systems, pressurization systems,
propellant management and storage, power
processing units
3 categories: chemical, electrical or less propellant
Chemical propulsion : ADN-based monopropellant
(« green ») (Ammonium dinitramide)
Size: 2U for 8U configuration
7*13*20 cm for 12U configuration

---
Command and data handling
Size: 9,8*9,5*0,9 cm
Command handling: Receive, validate, decode and
distribute commands
Data handling: gather, process and format spacecraft
housekeeping
Mission data: downlink, on board use and storage

---
Attitude determination and control system
Actuators: to supply the control torque
Reaction wheel: size 9,25*9,25*5,13 cm
Magnetorquer: size 10*10*2 cm
Attitude sensors: to determine the position of a reference body
Star tracker: size 4,2*4*8,3 cm

---
Electrical power system
Energy conversion into electrical power, energy storage, power regulation, distribution and control
Solar array as primary source (design by the power budget)
secondary battery (rechargeable): Lithium-ion battery with a storage capacity of 45 Wh, for eclipse and time of shadows
Size: 9*9,6*5,7 cm

---
COMMUnication system
Carrier tracking, command reception/detection, telemetry modulation/demodulation, ranging and subsystems operations
S-band transmitter (9,5*4,6*1,5 cm)
S-band patch antenna (5*5*0,32 cm)

---
Payload
Exposure of the Mini-EUSO = focal length / lens diameter = 1,2
Lens diameter: 12,5 cm
Focal length: 15 cm
MAPMT:
24*24 = 576 pixels of
3 mm

---
8u configuration
No extra battery, only 4 photomultipliers

---
12U configuration

---
Link budget
Frequency used: around 2200 MHz (S-band), and data rate of 8,22 Mbps
Equivalent Isotropic Radiated Power:
Total space losses:
Path losses: with
Pointing losses:
Link losses:
With the polarization mismatch, the loss due to atmospheric gases, the rain attenuation and the loss due to ionosphere
System noise temperature:
Normalized signal-to-noise ratio:
Pt : transmission power
Gt: patch antenna gain
Lt : insertion loss
δ=10° the elevation angle
e=10° the pointing error
ϴ=200° the patch antenna bandwidth
= 25K the receiving antenna noise temperature (ground station)
To=290K the reference temperature
F=1+(Tr/To) = 1,26 with Tr = 75K
Lr = 0,5 dB line losses

---
Link margin:

---
Power budget
Orbit
Orbital period for Sun-synchronous orbit: for an altitude of 800 km
Inclination : so at 800 km
Declination angle of Earth: +23,5° on June 31st and -23,5° on December 21st (6 months)  0,26° per day
Shadow?
 so α = 0,002° , then β = 89,998°
Cos (ϴ) = 0,88 so ϴ = 27,3°

---
Limit = 27,3°
Our case:  shadow between -18,6° and -23,5° and +18,6° and +23,5°  38 days with a part of the orbit in shadows
Part of the orbit?
For the maximum angle of 32,2°, δ = 90°-32,2 = 57,8° and cos(δ) = x / 7178 km so x = 6074 km
 so chord/2 = 3825 km so chord = 7650 km
Orbit perimeter = 45 100 km
1 orbit = 45100 km in 6080 s so time of eclipse = (7650*6080)/45100 = 1020 s
And time of daylight = 6080 - 1020 = 5060 s

---
6 months: 145 days of full sunlight and 38 days of semi eclipse
145 days = 145*24*3600 = 12 528 000 s
38 days = 3 110 400 s = 511 orbits  511*1020 = 521 220 s of eclipse
        511*5060 = 2 585 660 s of daylight
So 6 months = 12 528 000 + 2 585 660 -21 600 = 15 092 060 s of daylight
521 220 + 21 600 = 542 820 s of eclipse
Average in 1 orbit :
6 months = 15 811 200 s
Time of daylight = (6080*15 092 060)/15 811 200 = 5804 s
Time of eclipse = 6080 – 5804 = 276 s
Annular solar eclipse

---
Power required during daylight:
Reaction wheel	Power consumption: / Ideale: 180 mW / Steady state (1000 RPM each): 600 mW / Peak: 6000 mW / DC voltage = 5V
Magnetic torquers	No activation = 175 mW / Full activation (3-axis) < 1.2 W / Activation level (nominal) : 0.2 Am2 / Supply voltage = 5V
Star tracker: / ST-1 / Sagitta	Power consumption = 1.2 W / Voltage = +5V, nominal power consumption < 1400 mW
COM: / Transmitter / Antenna	Input voltage = 3.3V nominal / Current draw = 1.5A / So power supply = 3.3 * 1.5 = 4.95 W / Input power > 10 W
C&DH	Power consumption > 4W / Input voltage range : 9V - 13V

---
Propulsion: / Micropropulsion / EPSS	Supply voltage = 12V / Maximum required power = 2W / System operating voltage = 12V
EPS: / IPBU / IPDU / IPCU / IPBP	Ideal consumption = 63 mW / Ideal consumption = 66 mW / Ideal consumption = 0.331 W for MPPT (sunlight only) / 0.066 W for MCU (sunlight and eclipse) / Storage capacity = 45 Wh (to fill the battery for the eclipse time)
Payload	30 W
TOTAL (max consumption)	6+1.2+1.2+5+10+4+2+0.063+0.066+0.331+0.066+45+30= 104.93 W / Margin of 50%  power required during daylight = 157,4 W

---
Power required during eclipse:
Power Battery Unit (iPBU) = 63 mW
Power Distribution Unit (iPDU) = 66 mW
Power Conditioning Unit (iPCU) = 66 mW
Magnetorquer (no activation) = 175 mW
C&DH = 4 W
We need around 4,37 W so with a margin of 50%, the power required during eclipse is 6,6 W
Battery storage?
1 battery = 45 Wh
Worst case eclipse = 6h
1 battery should be enough but 1 extra battery for redundancy

---
Pd = 157,4 W
Td = 5060 s
Xd = 0,9
Pe = 606 W
Te = 1020 s
Xe = 0,8
Id = 0,95
 = 15°
Fd = 0,005 (0,5%)
Ny = 2 years
Total solar array area: (for the worst case and not the average)
Gallium Arsenide cells
The required power:
Ideal flux:
Begining of Life flux:
End of Life flux: with
Total solar array area:

---
Different efficiencies:
PSA = 175,28 W for the average, and 176,55 W for the worst case
Efficiency (%)	ideal (W/m2)	BOL (W/m2)	EOL(W/m2)	ASA / (m) / Average Worst case		Length of 4 panels 0.2 * … m / Average Worst case		Cubic panel / Average Worst case
20	273.4	250.9	248.4	0.706	0.711	0.882	0.888	0.840*0.840	0.843*0.843
25	341.75	313.62	310.49	0.565	0.569	0.706	0.711	0.752*0.752	0.754*0.754
28	382.76	351.26	347.75	0.504	0.508	0.63	0.635	0.710*0.710	0.713*0.713
30	410.1	392.2	388.27	0.451	0.455	0.564	0.568	0.672*0.672	0.675*0.675

---
Deployment technique for cubic panel: for an efficiency of 30 %

---
Cost budget
Without the payload
Components	Price (€)
Solar panels (30% efficiency)  10 000 € per	4550
Reaction Wheel	Estimation = 8 000
Magnetorquer	9750
Star Tracker	Estimation = 40 000
COM: / Transmitter / Antenna	6 500 / 4 600
C&DH	Estimation = 8 000
EPS	Estimation = 9 000
Propulsion	Estimation = 100 000
Structure	Estimation = 12 000
Ground station	66 700
Total cost = 270 640 €

---
MASS budget
Without the payload
Components	Mass (g)
Solar panels (30% efficiency)  1	801
Reaction Wheel	665
Magnetorquer	195
Star Tracker	108
COM: / Transmitter / Antenna	75 / 62
C&DH	65
EPS	668,7 (with extra batery)
Propulsion	2600
Structure	2000
Total mass = 7,2 kg

---
Final configuration
12U configuration
9 Photomultipliers
Lens diameter = 12,5 cm
COM = S-band
Solar array = 0,45